Oleksii Gamov, Kharkiv Academic Lyceum №45 graduate
Mazanov Maksym, PHD student in the ITMO University (St. Petersburg)
Study of closed dynamical system based on the Kapitsa phenomenon (inverted pendulum)

---
Kapitsa stabilization and analogs
2

---
System description
The system – double oscillator.
It’s made out of mathematical and spring pendulums connected together.
k
g
For this system we came up with differential equations describing it’s movement:
x
m
L
θ
x ' ' = g + {M θ {'} ^ {2} L + M left (g − x ' ' right ) cos left [θ right ]} over {m} cos left [θ right ] − {k} over {m} x " (1)"
M
θ ' ' = − {g − x ' ' left [t right ]} over {L} sin left [θ right ] " (2)"

---
Correction check

---
Mode discoveries
For the Kapitsa pendulum and double oscillator we’ve initialized simulation with different starting parameters.
We’ve made plots for average mathematical pendulum position and deviation from it.

---
Mode discoveries

---
Mode №1

---
Mode №2

---
Mode №3

---
Mode №4

---
Effective dynamic potential
For this system we can’t find static effective potential. It can be approximately described with dynamic potential.
γ = sqrt {{k} over {m + M cos {left [θ right ]} ^ {2}}} " (4)"
{U} rsub {еф} = mgL left (− cos left [θ right ] + {{a} ^ {2} {γ} ^ {2}} over {4 gL} sin {left [θ right ]} ^ {2} right ) " (3)"
a = {left (m + M right ) g + sqrt {{left (m + M right )} ^ {2} {g} ^ {2} + 2 k left (MgL left (cos left [θ right ] − cos left [{θ} rsub {0} right ] right ) + {k {x} rsub {0} rsup {2}} over {2} − left (m + M right ) g {x} rsub {0} right )}} over {k} " (5)"

---
Dynamic effective potential
3
1

---
Effective dynamic potential plots

---
Experimental model
We’re adding friction to the systen and pereodic movement of the suspension point. This will allow system not to lose much energy on friction and will make it possible for stable nontrivial modes to exist.
x ' ' = g + {M θ {'} ^ {2} L + M left (g − x ' ' right ) cos left [θ right ]} over {m} cos left [θ right ] − {k} over {m} x + {f} over {m} " (3)"
θ ' ' = − {g − x ' ' left [t right ]} over {L} sin left [θ right ] " (4)"
f left [t right ] = k r left [t right ] − {F} rsub {тр} " (5)"

---
Modulation results

---
Results
New modes have been found.
Effective dynamic potential is proposed.
Analogies in other fields are proposed.
Experimental model is proposed.

---
Thanks for your attention!

---
Additional slide №1
θ ' ' L M = − M left (g − x ' ' right ) sin left [θ right ] " (2)"
m x ' ' = mg + T cos left [α right ] − k x " (1)"
T = M θ {'} ^ {2} L + M left (g − x ' ' right ) cos left [θ right ] " (3)"
x ' ' = g + {M θ {'} ^ {2} L + M left (g − x ' ' right ) cos left [θ right ]} over {m} cos left [θ right ] − {k} over {m} x " (4)"
θ ' ' = − {g − x ' ' left [t right ]} over {L} sin left [θ right ] " (5)"

---
Additional slide №2
T = {m x {'} ^ {2}} over {2} + {M left ({left (x ' + L θ ' sin left [θ right ] right )} ^ {2} + {left (L θ ' cos left [θ right ] right )} ^ {2} right )} over {2} " (1)"
V = {k {x} ^ {2}} over {2} − mgx − Mg left (x + L cos left [θ right ] right ) " (2)"
L = T − V = {left (m + M right ) x {'} ^ {2}} over {2} + {M left ({L} ^ {2} θ {'} ^ {2} + 2 x ' L θ ' sin left [θ right ] right )} over {2} + left (m + M right ) gx + MgL cos left [θ right ] − {k {x} ^ {2}} over {2} " (3)"
{d} over {dt} left ({δ L} over {δ dot {x}} right ) − {δ L} over {δ x} = 0 " (4)"
{d} over {dt} left ({δ L} over {δ dot {θ}} right ) − {δ L} over {δ θ} = 0 " (5)"
x ' ' = g + {M θ {'} ^ {2} L + M left (g − x ' ' right ) cos left [θ right ]} over {m} cos left [θ right ] − {k} over {m} x " (6)"
θ ' ' = − {g − x ' ' left [t right ]} over {L} sin left [θ right ] " (7)"

---
Additional slide №3
T = M left (g + x ' ' right ) cos left [π − θ right ] " (1)"
{F} rsub {"пр эф"} = mg + T cos left [π − θ right ] = mg + M left (g + x ' ' right ) cos {left [π − θ right ]} ^ {2} " (2)"
γ = sqrt {{k} over {m + M cos {left [θ right ]} ^ {2}}} " (4)"
{m} rsub {эф} = {{F} rsub {"пр эф ср"}} over {g} = m + M cos {left [θ right ]} ^ {2} "(3)"
− left (m + M right ) g {x} rsub {0} − MgL cos left [{θ} rsub {0} right ] + {k {x} rsub {0} rsup {2}} over {2} = − left (m + M right ) g a − MgL cos left [θ right ] + {k {a} ^ {2}} over {2} " (5)"
{k} over {2} {a} ^ {2} − left (m + M right ) g a + MgL left (cos left [{θ} rsub {0} right ] − cos left [θ right ] right ) + left (m + M right ) g {x} rsub {0} − {k {x} rsub {0} rsup {2}} over {2} = 0 " (6)"
a = {left (m + M right ) g + sqrt {{left (m + M right )} ^ {2} {g} ^ {2} + 2 k left (MgL left (cos left [θ right ] − cos left [{θ} rsub {0} right ] right ) + {k {x} rsub {0} rsup {2}} over {2} − left (m + M right ) g {x} rsub {0} right )}} over {k} " (7)"